Course:	AG-AMII-01.422		  Agriculture Mechanics II

# Unit 3:				Tractor Maintenance and Operation

Lesson 1:	Identifying Tractor Power Systems

Georgia Performance Standards: 	AG-AMII-3 a-e

Academic Standards:                        ELA12LSV1, ELA9RL5

# National Standards:

# Objectives: 		1. 	To gain an understanding of the major tractor 		                              systems and how they relate to tractor power.

# To identify components of major tractor systems.

# To identify the uses of major tractor system components.

# To correlate major tractor system parts and functions to servicing and maintaining tractors.

# Teaching Time:	   5 hours

Grades: 9-12

Essential Question: What are the major tractor power systems and how do they work?

Unit Understandings, Themes, and Concepts:

Students will gain an understanding of major tractor systems and their components, as well as how these systems are used and serviced.

Primary Learning Goals:

Students will be able to explain the usage, components, and servicing of major tractor systems.

Students with disabilities: For students with disabilities, the instructor should refer to the individual student's IEP to insure that the accommodations specified in the IEP are being provided within the classroom setting. Instructors should familiarize themselves with the provisions of Behavior Intervention Plans that may be part of a student's IEP. Frequent consultation with a student's special education instructor will be beneficial in providing appropriate differentiation within any given instructional activity or requirement.

Assessment Method/Type:

____ Constructed Response		____ Peer Assessment

_X__ Combined Methods		____ Selected Response

____ Informal Checks				____ Self Assessment

# References:

Safe Tractor Operation and Daily Care.  4th edition.  American Association for

Vocational Instructional Materials. Wintersville, GA ISBN 0-89606-056-X

John Deere Operator’s Manual.  John Deere Waterloo Works, Moline, IL 0MAR113290 Issue A6.

Silleto, Thomas A. & Dale O. Hull & Thomas A. Hoener & W. Forrest Bear.  Safe

Operation of Agricultural Equipment.  Hobar Publications.  Minneapolis,

MN.  1996.

FMO-Fundamentals of Machine Operation, Tractors, Deere & Company, Moline,

IL.1994.

# Materials and Equipment:

Tractor

Screen

Projector

Power Points:

Tractor Systems

NAPNewDevelopmentsWeb

Web Resources:

http://en.wikipedia.org/wiki/Tractor#Engine_and_fuels

http://www.farmtractormanuals.com/

http://www.howstuffworks.com/ Type in system example “cooling system”

http://www.howstuffworks.com/turbo.htm

http://www.howstuffworks.com/gear.htm

http://www.howstuffworks.com/gear-ratio3.htm

http://www.howstuffworks.com/differential.htm

http://www.howstuffworks.com/clutch.htm

http://www.howstuffworks.com/engine1.htm

http://www.howstuffworks.com/diesel.htmm

http://www.howstuffworks.com/bearing.htm

http://www.howstuffworks.com/camshaft.htm

Georgia Performance Standards: 	AG-AMII-3 a-e

AG-AMII-3:  Students will implement a tractor maintenance and operation program.

a. 		Explain a tractor maintenance program.

b. 	Develop a detailed tractor maintenance calendar using the manufacturer=s service recommendations.

c. 	Interpret service manual for tractor maintenance.

d. 	Interpret a service manual for a tractor.

e. 	Perform basic service and maintenance recommendations on a tractor.

Academic Standards:                        ELA12LSV1, ELA9RL5

ELA9RC2 The student participates in discussions related to curricular learning in all subject areas.

ELA12LSV1 The student participates in student-to-teacher, student-to-student, and group verbal interactions.

ELA9RL5 The student understands and acquires new vocabulary and uses it correctly in reading and writing.

ELA10W3 The student uses research and technology to support writing.

MM1A3. The student solves simple equations.

MA1P1. The student solves problems (using appropriate technology).

MA1P3. The student communicates mathematically.

SCSh2 The student uses standard safety practices for all classroom laboratory and field investigations.

SCSh3 The student identifies and investigates problems scientifically.

SCSh4 The student uses tools and instruments for observing, measuring, and manipulating scientific equipment and materials.

SP1 The student analyzes the relationships between force, mass, gravity, and the motion of objects.

SPS5 The student compares and contrasts the phases of matter as they relate to atomic and molecular motion.

SPS7 The student relates transformations and flow of energy within a system.

# Teaching Procedure

# Introduction and Mental Set:  A tractor is a complex machine.  It takes a lot of components working together to keep a tractor operational.  In order to carry on proper service and maintenance of a tractor, you must understand how the components work together to keep the machine running and productive.

TRACTOR SYSTEMS

- SEE ACCOMPANYING POWERPOINT- TRACTOR SYSTEMS

I.  Tractor Engines

  - Engine- Classification

- With the demise of steam powered tractors in the late 1800’s, most modern tractors are equipped with internal combustion engines.

- Internal combustion engines are identified by the number of strokes in the cycle and by the type of fuel that is used to run them.

  - Common Tractor Engine Classifications.

- 4 stroke Cycle

  - Diesel

  - Gasoline

  - LP

- 2 Stroke Cycle

  - Internal Engine Parts

  - Cylinder

  - Piston

  - Connecting Rod

  - Crankshaft

  - Camshaft

  - Intake Valve

  - Exhaust Valve

  - 4 Stroke Cycle

| Name of Stroke | Piston | Intake Valve | Exhaust Valve | Crankshaft |
| --- | --- | --- | --- | --- |
| Intake | Down | Open | Closed | ½ revolution |
| Compression | Up | Closed | Closed | 1 revolution |
| Power | Down | Closed | Closed | 1 ½ revolutions |
| Exhaust | Up | Closed | Open | 2 revolutions |

II.    Major Tractor Systems

On-line reference:  http://www.fanshawec.on.ca/disability/ld/apprentice/chapter12.htm

A.    Intake System

Parts/ Uses

    - Pre-cleaner- serves to catch particles before entering air cleaner.  Creates “vortex” or air swirl.

    - Air Cleaner- keeps 99% of dust particles from entering engine and causing wear.

        - Inner filter- should never get dirty- Safety valve

        - Outer filter- should be serviced and changed.

    - Connecting Hoses/Tubes – makes connections from pre-cleaner to air cleaner to manifold. Clamps should make air tight connections.

    - Intake Manifold-  delivers air(diesel) or air/fuel mix(gasoline/LP) to each cylinder.

    - Intake Valve- opens to allow air or air fuel mix into cylinder during intake stoke. Closes to seal combustion.

    - Turbocharger (if used)- provides more air to cylinder to boost power. Powered by exhaust.

    - Intercooler (if used)- provides cooling to air to allow more air to be forced into cylinder increasing horsepower

- Exhaust System

Parts/ Uses

1. Exhaust Valve- opens to allow burnt gases to escape

During  exhaust stroke.  Closes to seal combustion.

2. Exhaust Manifold- Combines cylinders together to form

one Pipe for the elimination of exhaust gases.

3.  Muffler- Quiets engine noise and eliminates sparks.

        - Reverse Flow

        - Straight Through

- Exhaust Cap (if used)- Prevents rain, insects, debris, etc

from entering engine while at rest.

C.    Lubricating Systems- Full Flow and By-Pass

Parts/ Uses

    - Crankcase Reservoir (Oil Pan)-  Holds oil reserve for

Engine use.  Retains particles cleaned from oil for changing.

2.  Oil Pump-  Provides pressure to circulate oil through the

system.

3.  Oil Filter-  Provides cleaning/ filtering of solid particles

from oil supply.

4.  Oil Passages-  allows oil to pass through engine block to

areas that need lubrication.

5.  Pressure Regulating Valve- regulates oil pressure.

6.  Oil gauge/light-  provides the operator with indication of

Oil mpressure.

- Oil goes to:

-  Camshaft Bearings

-  Crankshaft main bearings

-  Valve train

      - Cylinder Walls

D.Electrical System

Parts/ Uses

- Battery- stores electrical power for systems.

    - Ground Cable (negative)- connects battery to frame for

grounding.

3.  Key Switch- connects battery power to starter and

Tractor systems.

4.  Ammeter gauge-  gives the operator a reading of battery

charge.

5.  Voltage Regulator- regulates output voltage from

alternator to battery.

6.  Starter Solenoid- engages power to starter.

7.  Starter- spins engine flywheel to crank.

8.  Distributor- “distributes” electrical power (spark) each

spark plug and cylinder.

    - Coil- increases electrical voltage to make spark ‘Jump” the

gap.

    - Alternator- provides battery charging.

    - Spark Plug (gasoline only) provides ignition of compressed

gases in each cylinder by making spark “jump” the gap.

11. Power Cable (positive)- connects battery positive to

Electrical connections requiring power usually via a fuse

panel for protection.

  - Cooling Systems – Air cooled and Liquid cooled

Parts/ Uses

1.  Radiator- Holds Coolant, provides heat exchange with

air (convection) to cool engine.

2.  Coolant Holding Tank (Plastic)- provides fluid exchange with

radiator. Recovery and storage.

3.  Pressure Cap- Keeps liquid from exiting radiator. Keeps debris

from entering radiator. Provides pressure on system to

increase boiling temperature. 1lb pressure = 3 degree increase

4.  Fan-  draws air through radiator to facilitate heat exchange

And cooling.

5.  Fan Belt- connects engine power to water pump to circulate

coolant.

6.  Water Pump- the “heart” of the system.  Circulates liquid

coolant through system to absorb heat from the

block (conduction).

7.  Water Jacket- passages within the engine block to allow liquid

to circulate and absorb heat.

8.  Thermostat- device that is controlled by the temperature of

coolant. Closes when cold to hold coolant in block until

operating temperature is reached usually 180 degrees or

above. Opens at operating temperature to allow coolant

circulation to radiator.

9.  Connecting(Radiator) Hoses- connect upper and lower

radiator ports to engine block for exchange of coolant.

10. Liquid (Coolant)-  Distilled water and antifreeze combine in

recommended ratios to provide cooling and to prevent

freezing of the liquid in winter months.

Three types of antifreeze available:

        - Ethylene Glycol- Permanent anti freeze.

Will not boil away. Poisonous if ingested.

        - Alcohol base- will boil away.

        - Environmental friendly- “Sierra” non-

poisonous.

F.  Fuel Systems

1.  Gasoline

Parts/ Uses

a.  Fuel Tank- holds reserve fuel for engine use.

b.  Fuel Pump- transfers fuel from tank to carburetor.

c.  Carburetor- atomizes fuel and mixes it with air in

correct proportions and delivers it to the cylinder via

the intake manifold.

- d.   Fuel Filter- removes solid residue from fuel before it

- enters the cylinder. Can have sediment filter to

- separate moisture from fuel also.

e.  Fuel Lines- connect the fuel tank to the carburetor to

- provide fuel to the engine.

2.  Diesel

Parts/Uses

        - Fuel Tank- holds reserve fuel for engine use.

        - Fuel Pump- transfers fuel from tank to injection pump.

        - Fuel Filters- removes solid residue from fuel before it enters the cylinder. Can have sediment filter to separate moisture from fuel also.

        - Injection Pump-  Moves , meters, and times fuel

to the injector nozzles.

        - Injector Nozzle-  Atomizes(fine spray) and

delivers fuel to cylinder in correct amount and

pattern.

3.  Liquid Petroleum (L P)

Parts/ Uses

a.  Pressurized Fuel Tank- holds reserve fuel for engine

use. The pressure keeps the highly volatile gas in liquid

form. A space for vapor is left at the top.

- b.  Fuel Strainer-  cleans the liquid fuel. Normally has a

- solenoid valve to permit fuel flow only when ignition is

turned on.

c.  Converter-  changes the liquid fuel to vapor by warming it

- and then reducing the pressure of the vapor.

- d.  Carburetor-  mixes the fuel vapor with air in the proper ratio

- for combustion.

G.  Hydraulic System

1.  Open- center-  good for the operation of one function.

Complications arise when controlling more than one

Function. System gets complex.

    - Closed-center-  good for more than one function.

Accumulator “stores” energy. Safer because system still

operates after engine has been turned off.

Parts/ Uses

1.  Reservoir- stores the oil, keeps oil clean, free of air, and

relatively cool.

2.  Accumulator or Pump- Converts hydraulic energy to

mechanical energy.

3.  Cooler-  cools hydraulic oil.

    - Valves-  controls direction, flow rate, and pressure of hydraulic

oil.

5.  Lines-  connects hydraulic components for fluid flow. Under

high pressure. Do not check for leaks with hands. Use a

piece of cardboard.

6.  Fluid-  hydraulic fluids lubricate, cool , and protect the system

from rust and corrosion.

7.  Filter-  cleans the fluid of contaminates.

8.  Cylinders-  operate loads.

- Motors-  provide continuous rotary output to equipment.

H.   Drive Train

Parts/ Uses

1.  Clutch-  transmits power from the engine to the transmission

and provides a means of starting and stopping power

flow to the transmission.

2.  Transmission-  train of gears that transfers and adapts the

engine power to the drive wheels.

3.  Differential-  transmits power from the output shaft of the

transmission to the drive axles. It allows the two drive

wheels to rotate at different speeds while each still propels

its share of the load.

4.  Final Drives-  provides the final reduction in speed and

increase in torque to the drive wheels.

###### Have students participate in Operation Labs.

- Overview of labs:  Labs are listed in order.  Each student,  regardless of prior experience will proceed through the labs in order. Each lab must be mastered with a minimum of 80% to proceed to the next lab. Students will participate every lab time at the level they have attained after lab 4. Some may need time practicing after school to keep up with class. Students will be given a final lab grade for each lab completed as well as daily participation grades.  Beginning ability should be factored into final grade.  Some students will not reach the final lab in the time alloted but have participated and made progress. Any intentional breach of safety rules will result in student returning to lab 1 in after school remediation.

( Labs are listed in order, for simplicity all labs applicable  to  the entire TRACTOR OPERARATION AND MAINTENANCE COURSE are listed. Choose lab or labs to be used with this lesson and continue with future lessons as time allows. Labs are designed to follow the order suggested but alternating of labs with Tractor Operation and Maintenance class work is recommended.)

  - LAB 1- Tractor Driving Course Set-up

Set up tractor Course according to Ag Tractor and Machinery

Operation and Maintenance CDE Bulletin.

  - LAB 2- Tractor Parts Identification

    - Make tags for parts numbered 1-50

    - Gather students around tractor in a group.

    - Assign individual students to attach tag to the part identified by that number on the tractor as assigned by teacher sheet.  (if student does not know location of part-let other students direct them to part)

    - After students have tagged parts assigned- have them write down names of parts and uses of the part on following chart for study.

OR

- Make tags for parts numbered 1-50

- Teacher puts tags on selected parts

- Assign student to find the part of the number you call out.

- After students have tagged parts assigned- have them write down names of parts and uses of the part on following chart for study.

- AFTER STUDENTS HAVE IDENTIFIED PARTS BY ONE OF THE METHODS- TALK ABOUT USES AND HAVE STUDENTS FILL OUT CHART

CHART

| Number of Part | Name of Part | Description/ Use(s) |
| --- | --- | --- |
| * = | All Tractors may not have |  |
| 1 | Steering Wheel | Turn steering tires (front usually) |
| 2 | Steering Tire (front) | Direct tractor direction |
| 3 | Drive Tire (rear) | Power Tractor |
| 4 | Seat | Operator Comfort |
| 5 | Seat Belt | Keep Operator in Safety Zone |
| 6 | ROPS | Operator Safety (rollover protection) |
| 7 | Pinch Point(Safety) Labels | Operator Safety(stay clear) |
| 8 | Warning Flashers | Warns others of tractor in operation(amber) |
| 9 | Light Switch | Turns light on/ off |
| 10 | Tail Light | Indicated rear of tractor to traffic(red) (powered) |
| 11 | Headlights | Light up front of tractor path(white) |
| 12 | Utility (work) Light | Light up rear of tractor( equipment) |
| 13 | Reflector | Reflects headlights from rear traffic(red)(unpowered) |
| *14 | Left Turn Signal | Indicates tractor turning left(amber) |
| *15 | Right Turn Signal | Indicates tractor turning right(amber) |
| 16 | Draw Bar | Implement hook-up |
| 17 | Clutch pedal | Engages/ disengages clutch for starting/ stopping tractor motion |
| 18 | Right Brake Pedal | Locks Right Drive Tire (rear) |
| 19 | Left Brake Pedal | Locks Left Drive Tire (rear) |
| 20 | Foot Throttle Pedal | Increases tractor RPM (speed) (variable) |
| 21 | Hand Throttle Lever | Increases Tractor RPM(speed) constant |
| 22 | PTO Control Lever | Engages/ disengages PTO shaft |
| 23 | Gear Shift Lever | Select Forward/ Reverse Gear |
| *24 | Shuttle Shift Lever | Shuttle from Forward to Reverse and Speeds without clutch |
| 25 | Shift Pattern Decal | Provides gear position and speed(speedometer) |
| 26 | Key & Switch | Engages power to parts from battery( may include solenoid for fuel shut-off) |
| 27 | Range Lever / Hi-Lo | Select Range ( high/ Low) for gears |
|  | Dash Gages |  |
| *28 | a. Air Filter Restriction | Indicates air filter needs cleaning/ changing |
| 29 | b. Coolant Temperature | Indicates Engine operating temperature |
| 30 | c. Hour Meter | Indicates hours of operation of tractor |
| 31 | d. Fuel Gauge | Indicates amount of fuel in tractor tank |
| 32 | e. Oil Pressure | Indicates engine oil pressure |
| 33 | f. Alternator/ Battery | Indicates battery charge |
| 34 | g. Tachometer | Indicates engine speed in Revolutions per minute |
| *35 | Manual Fuel Shut-off | Pull to shut off Diesel Engine |
| *36 | Parking Brake Lever | Pull to set parking brakes when off tractor |
| 37 | Differential Lock Pedal | Engage to lock drive axles together(positive traction) |
| 38 | Draft Control lever | Controls lift arms when implement is in working position |
| 39 | Position Control Lever | Controls lift arms when implement is in transportation position |
| *40 | Remote Hydraulic lever | Controls flow of hydraulic fluid to remote cylinders on implements |
| *41 | Hydraulic Quick Coupling | Provides connections for remote hydraulic hoses |
| *42 | 4 Wheel Drive Lever | Engages front wheel assist to let front wheels pull |
| 43 | SMV Sign | Required by law on vehicles operating on roads at less than 25 mph |
| 44 | Tool Box | Storage of tools |
| 45 | Left Lift Arm | Left hydraulic arm of three point hitch-hooking up implements |
| 46 | Right Lift Arm | Right hydraulic arm of three point hitch-hooking up implements |
| 47 | Top Link | Center hook-up point of three point hitch- adjust level of implement |
| 48 | PTO Cap | Protects operator from PTO shaft when not in use |
| 49 | PTO Shield | Protects operator from PTO shaft when in use |
| 50 | PTO Shaft | Provides tractor power to implements and equipment |
| 51 | Transmission Dipstick | Indicates level of transmission fluid |
| 52 | Rear End Dipstick | Indicates level of Rear end oil |
| 53 | Engine Oil Dipstick | Indicates level of Engine oil |
| 54 | Power Steering Dipstick | Indicates level of power steering fluid |
| 55 | Pre- Cleaner | Removes large particles from air before they get to the air filter- provides swirling action to air |
| 56 | Dust Unloading Valve | Daily check point for air filter |
| 57 | Outer Air Filter(Primary) | Provides air cleaning( filtration) for engine- removed dust and dirt(will get dirty) |
| 58 | Inner Air Filter (secondary) | Provides safety filter for outer filter- (should never get dirty) |
| 58 | Muffler | Provides quieter operation for engine and arrests sparks |
| *59 | Muffler Cap | Provides engine protection from rain/ particles entering engine when not running |
| 60 | Fuel Cap-Fill | Provides access to fuel tank when off- protection when on |
| 61 | Hydraulic Filter | Provides filtering(cleaning) of hydraulic fluid |
| 62 | Fuel Tank (Gravity feed) | Provides fuel storage for tractor engine operation |
| *63 | Fuel Filter- Water | Separates water from fuel |
| 64 | Fuel Filter- Solid | Filters (cleans) solids from fuel |
| 65 | Oil Filter | Filters (cleans) solids from engine oil |
| 66 | Power Steering Pump | Provides storage of power steering fluid and pressure for operation |
| 67 | Engine Oil fill Port/ cap | Provides point of access for adding engine oil-protection when on |
| TEST 1 | PARTS |  |
| 68 | Battery | Provides power for operation of electrical parts |
| 69 | a. Battery Caps- Fill | Provides access to fill battery-protection when on |
| 70 | b. Positive Battery Terminal | Provides power from battery to electrical parts |
| 71 | c. Negative (ground) Terminal | Provides ground to tractor chassis |
| 72 | Radiator | Provides for removal of heat from engine |
| 73 | a. Radiator Cap | Provides system pressure, access to radiator for fill, protection |
| 75 | c. Radiator Hoses | Provide connection from radiator to engine |
| 76 | d. Thermostat | Keeps coolant in engine until operating temperature has been reached- controls engine temperature |
| 77 | e. Fan | Provides air flow through radiator for heat removal |
| 78 | f. Fan Belt | Connects engine power to auxillary equipment on front of engine |
|  | g. Coolant pump (water pump) | Circulates coolant through engine and radiator |
| *79 | Carburetor (Gasoline) | Provides mixing of air and fuel for gasoline engine |
| *80 | Spark plugs (Gasoline) | Provides fire to ignite gasoline |
| *81 | Distributor (Gasoline) | Provides ignition (fire) to spark plugs |
| *82 | Injector Pump (Diesel) | Meters diesel fuel to injectors and controls engine timiing |
| *83 | Injector Nozzle (Diesel) | Controls(sprays) fuel entering cylinder- for ignition and running |
| ADD OTHERS AS NEEDED |  |  |

C.    LAB 3- Operation of Tractor Controls- Have students operate the

following tractor controls with Tractor stationary.

    - Key Switch- Cranking

    - Hand Throttle

    - Foot Throttle

    - PTO

    - Hydraulic Lift

    - Headlights

    - Warning Lights

    - Gear Patterns

    - Range Patterns

    - Brakes- Separate

    - Clutch Pedal

    - Parking Brake

    - Differential Pedal

    - Blinkers (opt)

    - Horn (opt)

D.	LAB 4- Tractor Operation

Set up 5 poles in a straight line approximately twenty feet apart.

Teacher should ride with student until student has proven ability to operate tractor safely !

    - Pole Course 1- Tractor Only- Forward and Reverse

weave through course in low range ( gear 1-3). May have	   students stop and shift to high range –low gear. Have students drive tractor around poles to opposite end of the course (with teacher on board for safety) . Student should touch last post with front of tractor, then return to the point of origin in reverse.

    - Pole Course 2-  Tractor with two wheel trailer.  Weave

between stakes making wide turns.  Make wide turn at end

and return still in forward direction. (DO NOT ATTEMPT TO BACK AT THIS POINT!)

a. Skills obtained:

- Clutch Operation

- Brake Operation

- Gear Selection

- Range Selection

- Accelerating

- Braking

- Maneuvering

- Forward movement

- Reverse movement

b. Skills Graded for elevation to next lab at 80 %

minimum.

- 1)  Operation of:

- a)  Hand Throttle

- b)  Foot Throttle

- c)  Steering

- d)  Clutch

- e)  Brakes

- 2)  Safety

a)  Speed

b)  Seat Belt

c)   Proper Dismount

E.	LAB 5- Tractor Operation

Maneuvering Tractor/ Trailer through the Curve.  Have student maneuver tractor and two wheel trailer through the curve of the tractor course set up in lab 1.  Teacher and student have option of teacher riding on tractor if teacher has approved individuals safety in preceding lab.

Score lab by number of markers scraped or knocked down and safety ( seat belt, speed, etc).  Student must attain a mastery of at least 80% to move to next lab.

F.	LAB 6- Tractor Operation

Overview of lab 6:  Student will begin with trailer and tractor in course barn set up in lab 1.  The student will hitch up the trailer,

mount the tractor properly, fasten their seat belt, crank the tractor, select a range (low) and a gear(1-3), release the parking brake, and pull out of the barn.  Student will proceed to boundary marker( 100 ft from back of barn as set up in lab 1), STOP, select reverse gear(low range) and back trailer to post teacher has set up in the center of the barn located in front of the barn. (Teacher may option to ride with student to teach them to back or give directions from the ground).  Students will back to pole until they can center the pole on the back of the trailer.  The teacher will then move the post and allow student to back into barn.

    - Hitching/ Unhitching Trailer

    - Pulling out of Barn

    - Backing the Trailer to post.

    - Backing Trailer into barn.( 12 “ clearance)

    - Separating Brakes (Backing with Brakes)

- LAB 7- Tractor Operation

Driving entire tractor course as set up in lab 1.

Lab overview:  Student will begin with the tractor only at designated starting/ ending point as provided for in the Tractor Operation and Maintenance CDE Bulletin. (opposite , facing the barn). The two wheel trailer will be in the barn. The student will crank the tractor, select a range and gear, release the parking brake and proceed at a safe speed to the barn containing the trailer. They will then back the tractor into the barn, shut off the tractor, lock the parking brake, release their seat belt, and exit the tractor correctly.  The student should then proceed to attach the trailer to the drawbar of the tractor.  Once the trailer has been attached, the student will mount the tractor and proceed as outlined in the procedure used at the beginning line to pull the tractor and trailer out of the barn.  Once out of the barn, the student will proceed to pull the trailer through the 15 degree curve, return the trailer to the barn, unhitch , and return the tractor to the starting point.

Student should be graded according to score sheet contained in Tractor Operation and Maintenance CDE Bulletin.

# Summary

An understanding of the components of the major tractor systems is a necessary part of being able to maintain, service, troubleshoot, and repair these machines.  Developing a basic understanding of the parts and uses of the major tractor systems will enable you to carry on a successful maintenance program resulting in better machine performance and useful life.

# Evaluation

# Written test

Laboratory activity

Individual Learning Activity

Lesson:	Identifying Tractor Power Systems

Assignment:	Choose one of the topics below and research it. Write a report on your findings that answers the question or explains the concept and shows why it is relevant to your life.

# To gain an understanding of the major tractor 		systems and how they relate to tractor power.

# To identify components of major tractor systems.

# To identify the uses of major tractor system components.

- To correlate major tractor system parts and functions to servicing and maintaining tractors.

Minimum Requirements:

1. Paper must be typed in 12 point font and at least one page in length. The paper may be double-spaced.

2. At least two credible references must be properly cited.

3. All work must be original. No plagiarism! Any use of another’s ideas without giving credit will result in a zero.

4. Papers will be graded on content (amount of good information, accuracy, etc.) and mechanics (grammar, spelling, and punctuation.)

Due Date:

Points/Grade Available:

Individual Learning Activity Rubric

| Content - offers current information on the topic chosen, thoroughly covers each aspect of the question, and demonstrates understanding and mastery of the lesson. The paper should include information and issues of state and local importance. | 35 pts. |
| --- | --- |
| Critical Analysis - logical process of analyzing and reporting information that examines and explains the topic selected. The paper should go beyond simply listing facts and must include why the concept is relevant to the student’s life. | 25 pts. |
| Organization- The paper should have an orderly structure that demonstrates a logical flow of ideas. | 15 pts. |
| Mechanics- spelling, grammar, punctuation, font size, double spacing, citation, etc. Essentially, the paper should meet all specifications and be executed following rules of proper written English. | 15 pts. |

Group Learning Activity

Lesson: 	Identifying Tractor Power Systems

Assignment: 	Choose one of the topics below and research it. With your group, prepare a presentation to teach the class your concept.

# To gain an understanding of the major tractor systems and how they relate to tractor power.

# To identify components of major tractor systems.

# To identify the uses of major tractor system components.

            - To correlate major tractor system parts and functions to servicing and maintaining tractors.

Your presentation should include the following:

- A lesson plan outlining exactly what your group will teach and how the information will be taught

- A Power Point of at least twelve slides

- Notes containing the information the class will be responsible for (these can be printed and given to the class, written on the board, or part of the Power Point). A copy of the notes will be turned in to the instructor.

- Some type of interactive activity for the class (game, problem solving activity, interactive model, etc.)

- Your group must also prepare an assessment for the class. This assessment can be written or oral, but should show the instructor that the class understands and has retained the material being taught.

Due Date:

Points/Grade Available:

All work must be original. No plagiarism! Any use of

another’s ideas without giving credit will result in a zero

Group Learning Activity Rubric

| Lesson Plan – The group submits a thorough, detailed lesson plan highlighting the content and organization of their lesson. | 10 pts. |
| --- | --- |
| PowerPoint – The group presents a Power Point of at least twelve slides that contains information and pictures vital to the lesson with additional information or examples for enhancement. | 20 pts. |
| Interactive Activity – Some type of interactive activity is used to help teach the lesson. The activity should contribute to the mastery of content and involve the entire class in some way. | 15 pts. |
| Assessment – A fair, thorough assessment is prepared and administered based on the information presented to the class. Poor grades on the assessment by a few members of the class are excusable, but if the entire class has difficulty, the points awarded in this category may be lowered at the discretion of the instructor. | 15 pts. |
| Content – The group should cover the concept (within reason) in entirety. The group may study actual lesson plans to help decide what should be emphasized. | 25 pts. |
| Overall Effect – The group is prepared, enthusiastic, and interesting, and the lesson flows smoothly. | 15 pts. |

Presentation Learning Activity

Lesson:	Identifying Tractor Power Systems

Assignment:	Choose one of the topics below, research it, and prepare a presentation that answers the question or explains the concept and shows why it is relevant to your life.

# To gain an understanding of the major tractor systems and how they relate to tractor power.

# To identify components of major tractor systems.

# To identify the uses of major tractor system components.

4. To correlate major tractor system parts and functions to servicing and maintaining tractors.

Minimum Requirements:

Oral Report Option

1.   Write a paper on one of the topics and orally present your work to the class.

2.   Paper may be double-spaced and should be at least one page in length, resulting in a two to five minute presentation.

3.   At least two references must be properly cited.

4.   The presentation of the report will be graded secondary

to the content of the paper.

PowerPoint Option

- Presentation should be at least ten slides in length

- Presentation should include at least four photos.

- Presentation should be two to five minutes in length.

- Grammar and spelling will be graded by the same standards as any other written assignment.

- At least two references must be properly cited.

Poster Option:

- Prepare a poster that answers/explains one of the topics. You will present your poster to the class.

- Your poster should include both text and graphics that help communicate your research.

- At least two sources of information should be properly cited on the back of the poster.

- Neatness and appearance of the poster will be graded.

- Poster presentation should last two to five minutes.

Due Date:

Points/Grade Available:

For all presentations: All work must be original. No plagiarism! Any use of another’s work or ideas without giving proper credit will result in a zero.

Presentation Learning Activity Rubric

| Content- offers current information on the topic chosen, thoroughly covers each aspect of the question, and demonstrates understanding and mastery of the lesson. The presentation should include information and issues of state and local importance. | 40 pts. |
| --- | --- |
| Critical Analysis/Organization – The presentation shows a logical process of analyzing and reporting information that examines and explains the topic selected. The presentation should go beyond simply listing facts and must include why the concept is relevant to the student’s life. | 20 pts. |
| Presentation – The student makes a genuine effort to present, not just read the material. The student should present with confidence using techniques like eye contact and voice inflexion to make his or her point. Although content takes precedence over presentation, the experience of successfully presenting in front of a class is part of the basis of this assignment. | 25 pts. |
| Mechanics- spelling, grammar, punctuation, font size, double spacing, citation, etc. Essentially, the presentation should meet all guidelines set forth and should be executed in proper written English. For the poster, this includes neatness and appearance. | 15 pts. |

Essential Question:

What are the major tractor power systems and how do they work?

Vocabulary

Intake System

Exhaust System

Lubricating Systems

Electrical System

Cooling Systems

Fuel Systems

Hydraulic System